## Slide 1: Eye-tracking for Diagnosis of Visual Deficits
Sidhant raje
Jerry Zhang
Supervisor: Dr Luke hallum
Part IV Research Project 2019

## Slide 2: Research intent
Existing methods for detection of visual deficits
  Lack of quantitative measures
  Subjective
  Manual
  Expensive
Application of technology in diagnosis
  Computer-based systems can increase accessibility to testing
  Automated
  Portable
  Enable quantitative analysis for diagnosis as well as treatment

## Slide 3: Visual deficits
Strabismus
  Misalignment of visual axes
  Caused by disorder in the coordination of extraocular muscles
Complications
  High prevalence in children
  May lead to amblyopia (decreased vision) in the strabismic eye
  Lack of treatment during childhood may result in permanent vision loss
Four main types of strabismus

## Slide 4: Eye-tracking system
Ober Consulting Jazz-Novo eye-tracker
Jazz-novo eye-tracker
  Eye movements measured through infrared oculography
  Infrared emitters/sensors are located between the eyes
  Outputs resultant position left and right eye as a single gaze position
  High sampling frequency - 1kHz

## Slide 5: Experimental design
Characteristics of strabismus
  Misalignment of visual axes
  The eye used for fixation can alternate
Red (Left) and Blue (Right)
Dichroic Filters
Dichoptic presentation
  Enable viewing of independent images by each eye
  Analysis of visual capability of each eye

## Slide 6: Experimental design
Fixation test
  1 Hz alternation of red and blue stimuli at 9 locations
  Filters will allow the stimulus to be visible to one eye at a time
  Oscillation in gaze position may be present if the subject has misalignment in visual axes
9-point fixation test with red/blue alternations

## Slide 7: Experimental design
Tracking test
  Stimuli of both colours will displace horizontally and vertically
  Gaze position can be analysed against the target trajectory to quantify the tracking performance
Horizontal and vertical tracking test

## Slide 8: data acquisition
Calibration
  4-point calibration for fixation test
  2-point calibration for tracking tests (x2 sets)
  Acquire relative screen coordinates
Fixation Test Calibration Points
Tracking Test Calibration Points
1
1
2
2
Notes: To enable analysis of data points relative to screen points

## Slide 9: data acquisition
Trigger / Synchronisation
  White square flashes at start of event
  Read by Photodiode
  Output trigger (Binary 1 or 0) through Arduino Uno to Biosemi ActiveTwo
Photodiode and Trigger Setup

## Slide 10: data acquisition
Data Extraction
  Actiview software saves as BDF file
  Use Fieldtrip Toolbox in MATLAB to load BDF file
  Extract X, Y, and Trigger data
Fieldtrip Toolbox
  Open-source data analysis toolbox
  Reads BDF Header and stores specified channels to MATLAB variables
Jazz Novo SN 1060
Biosemi ActiveTwo
BDF File
MATLAB – (Fieldtrip)
X-Y Pos. & Trigger data
Data Analysis
Data Extraction Methodology

## Slide 11: Testing process
4-point Calibration & Fixation Test
Dichroic Filter (Red-Blue)
Dichroic Filter (Blue-Red)
4-point Calibration & Fixation Test
Dichroic Filter (Blue-Red)
2-point Calibration & Horizontal Tracking
2-point Calibration & Vertical Tracking
Dichroic Filter (Red-Blue)
2-point Calibration & Horizontal Tracking
2-point Calibration & Vertical Tracking
DATA ANALYSIS

## Slide 12: Results and analysis
Fixation Test
  Mean (Accuracy) - Standard Deviation (Precision)
  Fast Fourier Transform (FFT) of 1 Hz Oscillation
  Relative Gains (Fixation A1/Calibration A0)
*Test data from Subject-M1608
Fixation Test Data
FFT Analysis of first fixation point
Calibration Points

## Slide 13: Results and analysis
*Test data from Subject-M1608
Tracking Test Data
Calibration Points
Tracking Test
  Quantify ‘tracking’ ability
  Gain (Amplitude)
  Phase (Lag)
  Dominant minus Non-Dominant Eye

## Slide 14: Conclusion
  Use Eye-tracking system to classify between strabismic and ‘visually-normal’ subject
  Magnitude of oscillations at 1 Hz in all 9 gaze directions
  Relative gain (A1/A0) used to show significantly high magnitude oscillations
  Difference between DE and NDE used to illustrate tracking performance

## Slide 15: Future work
Further Testing of Subjects
  Strabismic subjects
  ‘Visually-normal’ subjects
Automated analysis via Machine Learning
  Classify type and severity strabismus autonomously using training data
Less invasive method
  Non-contact eye-tracker suitable for children
Mobile system
  Ability to use in clinical practices